ABSTRACT

The position and ratio size of branch in piping fitting are two important factors in ensuring the safety of piping system. This report highlights the simulation analysis of various positions of the branch pipes with 30o, 45o, 60o and 90o angles to the main pipe. The objective of the study is to study elastic behaviour including elastic stress distribution, stress concentration factor, and deformation characteristics of three full scale branch pipes under internal pressure with different geometric dimensions and lateral angle (sym. angle) by three-dimensional finite element methods. At the beginning, AutoCAD and CATIA software was used to design the structural design of the branch pipes and then followed by the use of ANSYS software to analyze the strength of the pipes under internal pressure.

ACKNOWLEDGEMENT

The author wishes to take the opportunity to express his utmost gratitude to the individual that have taken the time and effort to assist the author in completing the project. Without cooperation of these individuals, no doubt the author would have faced some minor-complications through out the research.

First and foremost the author’s utmost gratitude goes to the author’s supervisor Dr. Khairul Fuad Muhammad Rasyid. Without his guidance and patience, the author would not be succeeded to finish and complete the project. To both author’s parents, AP Aziz Nordin and Prof. Hasnah Mohd Sirat for supporting and providing all the needs from the beginning until the end.

To Mr. Farid bin Omar from Mechanical Engineering, thank you for your best cooperation and for assisting the author to complete his project.

To all individuals that has helped the author in any way, but whose name is not mentioned here, the author thank you all.

TABLE OF CONTENTS

CHAPTER 1:		INTRODUCTION						1

1.1	Back ground of the study						1

1.2	Problem Statement							1

1.2.1	Problem identification						2

1.2.2	Significant of the project					3

1.3	Objective								3

1.4	Scope of the study							3

CHAPTER 2:		LITERATURE REVIEWS AND THEORY		4

2.1	Introduction								4

2.2	Structural Analysis							4

2.3	Finite Element Analysis						6

2.4	Stress									8

2.5	Von Mises Equivalent Stress						11

2.6	Stress concentration factor						11

2.7	Piping									12

2.8	Summary								14

CHAPTER 3:		METHODOLOGY						15

3.1 	Introduction								15

3.2	Procedure identification						15

3.2.1	Phases in research procedure					17

3.3	AutoCAD software							18

3.4	CATIA software							18

3.5 	ANSYS analysis flow 						18

3.5.1	Preprocessing phase						19

3.5.2	Solution phase 						20

3.5.3 	Post processing phase						20

3.6	Summary								20

CHAPTER 4:		RESULT AND DISCUSSION				21

4.1	Introduction								21

4.2	Material Properties							21

4.3	AutoCAD design							23

4.4	CATIA design								24

4.4.1	CATIA branch pipe designs at 30o angle			25

4.4.2	CATIA branch pipe designs at 45o angle			28

4.4.3	CATIA branch pipe designs at 60o angle			30

4.4.4	CATIA branch pipe designs at 90o angle			32

4.5	ANSYS Analysis							20

4.5.1	ANSYS analysis of branch pipes at 30o angle		35

4.5.2	ANSYS analysis of branch pipes at 45o angle		41

4.5.3	ANSYS analysis of branch pipes at 60o angle		46

4.5.4	ANSYS analysis of branch pipes at 90o angle		51

4.5.5	Comparison between 30o, 45o, 60o and 90o angle		56

4.6	Summary								56

CHAPTER 5:		CONCLUSION & RECOMMENDATION		57

REFERENCES									59

APPENDICES									61

LIST OF FIGURES

Figure 2.1: Stress analysis of hoop and longitudinal stresses			8

Figure 2.2: Hoop stress along the cylinder						9

Figure 2.3: Longitudinal stress across the cylinder 					9

Figure 2.4: Geometries for piping branch junction and the terminology		12

Figure 2.5: Schematic of branch junctions with relevant geometric variables.	13

Figure 3.1: Flow chart of the research procedure					16

Figure 3.2: Steps involved during ANSYS V12.0 software				19

Figure 4.1: AutoCAD design of branch pipe at 30o angle				23

Figure 4.2: AutoCAD design of branch pipe at 45o angle				23

Figure 4.3: AutoCAD design of branch pipe at 60o angle				24

Figure 4.4: AutoCAD design of branch pipe at 90o angle				24

Figure 4.5: 0.25 d/D design of branch pipe at 30o angle				25

Figure 4.6: 0.3125 d/D design of branch pipe at 30o angle				25

Figure 4.7: 0.375 d/D design of branch pipe at 30o angle				25

Figure 4.8: 0.4375 d/D design of branch pipe at 30o angle				26

Figure 4.9: 0.5 d/D design of branch pipe at 30o angle				26

Figure 4.10: 0.625 d/D design of branch pipe at 30o angle				26

Figure 4.11: 0.75 d/D design of branch pipe at 30o angle				27

Figure 4.12: 0.25 d/D design of branch pipe at 45o angle				28

Figure 4.13: 0.3125 d/D design of branch pipe at 45o angle				28

Figure 4.14: 0.375 d/D design of branch pipe at 45o angle				28

Figure 4.15: 0.4375 d/D design of branch pipe at 45o angle				29

Figure 4.16: 0.5 d/D design of branch pipe at 45o angle				29

Figure 4.17: 0.625 d/D design of branch pipe at 45o angle				29

Figure 4.18: 0.75 d/D design of branch pipe at 45o angle				30

Figure 4.19: 0.25 d/D design of branch pipe at 60o angle				30

Figure 4.20: 0.3125 d/D design of branch pipe at 60o angle				30

Figure 4.21: 0.375 d/D design of branch pipe at 60o angle				31

Figure 4.22: 0.4375 d/D design of branch pipe at 60o angle				31

Figure 4.23: 0.5 d/D design of branch pipe at 60o angle				31

Figure 4.24: 0.625 d/D design of branch pipe at 60o angle				32

Figure 4.25: 0.75 d/D design of branch pipe at 60o angle				32

Figure 4.26: 0.25 d/D design of branch pipe at 90o angle				32

Figure 4.27: 0.3125 d/D design of branch pipe at 90o angle				33

Figure 4.28: 0.375 d/D design of branch pipe at 90o angle				33

Figure 4.29: 0.4375 d/D design of branch pipe at 90o angle				33

Figure 4.30: 0.5 d/D design of branch pipe at 90o angle				34

Figure 4.31: 0.625 d/D design of branch pipe at 90o angle				34

Figure 4.32: 0.75 d/D design of branch pipe at 90o angle				34

Figure 4.33: 0.25 d/D ANSYS analysis at 30o angle					35

Figure 4.34: 0.3125 d/D ANSYS analysis at 30o angle				36

Figure 4.35: 0.375 d/D ANSYS analysis at 30o angle				36

Figure 4.36: 0.4375 d/D ANSYS analysis at 30o angle				37

Figure 4.37: 0.5 d/D ANSYS analysis at 30o angle					37

Figure 4.38: 0.625 d/D ANSYS analysis at 30o angle				38

Figure 4.39: 0.75 d/D ANSYS analysis at 30o angle					38

Figure 4.40: Stress concentration factor versus d/D for 30o angle 			39

Figure 4.41: Maximum stress at 30o branch pipe					40

Figure 4.42: 0.25 d/D ANSYS analysis at 45o angle					41

Figure 4.43: 0.3125 d/D ANSYS analysis at 45o angle				41

Figure 4.44: 0.375 d/D ANSYS analysis at 45o angle				42

Figure 4.45: 0.4375 d/D ANSYS analysis at 45o angle				42

Figure 4.46: 0.5 d/D ANSYS analysis at 45o angle					43

Figure 4.47: 0.625 d/D ANSYS analysis at 45o angle				43

Figure 4.48: 0.75 d/D ANSYS analysis at 45o angle					44

Figure 4.49: Stress concentration factor versus d/D for 45o angle 			45

Figure 4.50: 0.25 d/D ANSYS analysis at 60o angle					46

Figure 4.51: 0.3125 d/D ANSYS analysis at 60o angle				46

Figure 4.52: 0.375 d/D ANSYS analysis at 60o angle				47

Figure 4.53: 0.4375 d/D ANSYS analysis at 60o angle				47

Figure 4.54: 0.5 d/D ANSYS analysis at 60o angle					48

Figure 4.55: 0.625 d/D ANSYS analysis at 60o angle				48

Figure 4.56: 0.75 d/D ANSYS analysis at 60o angle					49

Figure 4.57: Stress concentration factor versus d/D for 60o angle 			50

Figure 4.58: 0.25 d/D ANSYS analysis at 90o angle					51

Figure 4.59: 0.3125 d/D ANSYS analysis at 90o angle				51

Figure 4.60: 0.375 d/D ANSYS analysis at 90o angle				52

Figure 4.61: 0.4375 d/D ANSYS analysis at 90o angle				52

Figure 4.62: 0.5 d/D ANSYS analysis at 90o angle					53

Figure 4.63: 0.625 d/D ANSYS analysis at 90o angle				53

Figure 4.64: 0.75 d/D ANSYS analysis at 90o angle					54

Figure 4.65: Stress concentration factor versus d/D for 90o angle 			55

Figure 4.66: Maximum stress for 90o branch pipe					55

Figure 4.67: Stress concentration factor for various angles of branch pipe		56

Figure 5.1: Removal of inner part of branch pipe					58

LIST OF TABLES

Table 4.1: Material properties for branch pipe					21

Table 4.2: Model parameter								21

Table 4.3: Stress concentration factor for 30o angle under internal pressure		39

Table 4.4: Stress concentration factor for 45o angle under internal pressure		44

Table 4.5: Stress concentration factor for 60o angle under internal pressure		49

Table 4.6: Stress concentration factor for 90o angle under internal pressure		54